## Slide 1: EESI data analysis pipeline
From Tofware output to time series (e.g. for PMF)
General Overview of Jungfraujoch EESI dataset
Julian Weng
2025/03

## Slide 2
Input

## Slide 3: Input
Amus: Ion names & m/z
Time series of EESI data
Run number series of EESI data
Same dimension

## Slide 4: Input
EESI data matrix
Ions
Run numbers / time stamps

## Slide 5: Input
Autosampler dataframe
(sample IDs and types, sample & waterblank starting/ending times)

## Slide 6: Input
Sample info data
(Sampling dates, effective extraction volumes)

## Slide 7
Pre-processing and filtering

## Slide 8
Removing larges spikes/outliers
Based on primary ion signal

## Slide 9: Removing spikes
Define cutoffs (low & high) based on visual inspection of primary ion signal; make sure no real data points out of defined cutoffs Simply filter values out of cutoff range
Could be improved by more local filtering…but later steps also include filters
filtered
Before
After
Filtering is not very harsh (only big spikes removed)

## Slide 10
Assignment of run numbers to samples and waterblanks

## Slide 11: Assign RN to each sample and its corresponding waterblank
Using time information of autosampler df (EESI data needs to have same time, check for shifts due to time lags in computers)
…

## Slide 12: Assign RN to each sample and its corresponding waterblank
wb
sample

## Slide 13
For datapoints of each sample and wb:
Filtering of outlier datapoints based on median absolute deviation filter
(and excluding RN that only contain nan)

## Slide 14: median absolute deviation filter
Compute median of differences of each RN i to its sample median
Then for each RN, if difference / median(differences of all RN of this sample) lays above threshold => filter as outlier
Thresholds applied:
Sample: 2
Water Blanks: 3
Filtering should be done based on ion present in all samples! Primary ion or internal standard, not levoglucosan (as this is just random noise in some samples and all wb)

## Slide 15: median absolute deviation filter performance
Before
After
filtered

## Slide 16: median absolute deviation filter performance
Before
After
filtered

## Slide 17
Normalizations

## Slide 18: The logic behind normalization
Signal in EESI proportional to molar concentration of species in aerosol (in contrast to AMS)
Sensitivity (signal response per molecule in aerosol) species dependent
Therefore, no quantification of ‘unspiked’ species with internal standard (in contrast to AMS)
  Side note: Previously workflows, used to do it anyway as a very rough approximation, respecting the differences in molecular masses, including Na+, etc. <=> part of semi-quantification (now: quantification attempted by comparison of PMF factor output of quantitative AMS vs EESI)

## Slide 19: The logic behind normalization
What (apart from chemical structure) affects the relation ‘molar conc. in extract’ vs ‘signal in EESI’?
Inconsistent performance of the nebulization process
EESI spray fluctuations (spray position etc.)
Other inconsistencies in EESI performance?
Assumption for all effects: same behavior for all species with respect to these changes
Correct with
Primary ions aka reagent ions => Reflects EESI fluctuations
Internal standard => Reflects EESI & Nebulization fluctuations

## Slide 20: Normalization – Overview of current procedure
i) Point by point normalization (i.e. before averaging) with reagent ions (Na2I+ and Na2I+ (H2O))
=> for checking and evaluating internal standard performance throughout the measurements
ii) Point by point normalization (i.e. before averaging) with internal standard ions => That means primary ion normalized ions are getting normalized by primary ion normalized internal standards

## Slide 21: Waterblank – Sample Patterns: Primary ion
wb
sample
Samples with higher concentration => stronger primary ion depletion

## Slide 22: Waterblank – Sample Patterns: Internal standard sulfate
wb
sample
Expected under ideal conditions: similar levels for both, wb and sample
Expected under real conditions: higher levels for high concentration samples (as more internal standard brought to aerosol phase; at least that’s observation in AMS)
Observed: wb higher than samples, seems to scale with sample concentration => competition for reagent ion (reagent ion depletion?
Note: trends in good agreement with nitrate internal standard

## Slide 23: Waterblank – Sample Patterns: Internal standard sulfate (primary ion normalized)
wb
sample
Observation: wb and samples aligned closer
Primary ion is more depleted in high concentration samples, at same time lower internal standard intensity in high concentration samples (maybe due to more competition for primary ion) => these two effects compensate when doing the normalization

## Slide 24
Normalization by primary ions (reagent ions)

## Slide 25: Overview of primary ions (within the fit range currently applied)
Ion | Comment | Fit as (name in peak list) | m/z
Na2I+ |  | Na2I+ | 172.88347
Na3I2+ |  | I2Na3+ | 322.77771
Ion | Comment | Fit as (name in peak list) | m/z
Na2I(H2O)+ | Water cluster | Na2I(H2O)+ | 190.89403
Na3I2(H2O)+ | Water cluster | H2I2Na3O+ | 340.78827
Water clusters

## Slide 26: Why?
Why do we normalize by the reagent ion in first step, if later we normalize with internal standard (which is then already normalized by reagent ion, so effects cancel out)?
Normalizing with reagent ion can make sense:
Checking time series of internal standard signal, e.g. to get 'pure' effect of nebulization variability, matrix effects on internal standards, selection of internal standard ions
If normalization with internal standard is done based on sample average rather than point by point

## Slide 27: Considerations for normalizing by primary ions
Primary ion signal reflects EESI fluctuations
But: signal intensity also reflects on sample concentration, as reaction with sample ions leads to primary ion signal depletion
=> Normalization by primary ion introduces a bias with respect to sample concentration

## Slide 28: Normalization by primary ions
For each run number and ion j:
Sum of primary ion and its water cluster

## Slide 29: Sulfate internal standard – before and after normalization with primary ion
Before
After

## Slide 30
Normalization by internal standards

## Slide 31: Overview of sulfate internal standard ions
Ion | Comment | Fit as (name in peak list) | m/z
Na3[34S]O4+ | Considered important | Na3[34S]O4+ | 165.92
Na3[34S]O4(NaI)+ | Considered important | INa4[34S]O4+ | 315.82
Ion | Comment | Fit as (name in peak list) | m/z
Na3[34S]O4(H2O)+ | Considered minor | Na3[34S]O4(H2O)+ | 183.93
Na3[34S]O4(NaI)(H2O)+ | Considered minor | H2INa4O5[34S]+ | 333.83
Water clusters

## Slide 32: Overview of nitrate internal standard ions
Ion | Comment | Fit as (name in peak list) | m/z
Na2[15N]O3+ | Considered important | Na2[15N]O3+ | 108.96
Na2[15N]O3(NaI)+ | Considered important | INa3[15N]O3+ | 258.86
Ion | Comment | Fit as (name in peak list) | m/z
Na2[15N]O3(H2O)+ | Considered minor | - | 126.97
Na2[15N]O3(NaI)(H2O)+ | Considered minor | - | 276.86
Water clusters

## Slide 33: Considerations for normalizing by internal standards
Primary ion normalized ions are getting normalized by primary ion normalized internal standards
=> Primary ion normalization effect cancels out

## Slide 34
Averaging Effective extraction volume correction
Water blank subtraction

## Slide 35: Averaging
For each sample and its corresponding waterblank:
Compute average of normalized data (using assigned RN for each sample and its wb)
Primary ion normalized
Internal standard normalized
Normalized EESI data
Autosampler dataframe with different averages for s:sample and wb: waterblank
…

## Slide 36: Effective extraction volume correction – Background
Problem: for samples where filters were extracted, effective spiking volume does not equal the theoretical one, as some volume is held back in vials, syringes and filter punches
=> Internal standard concentration effectively changed (higher than expected)
Corrected for by weighing vials before (empty) and after extraction and applying a correction factor
Theoretical for JFJ campaign: 12 mL
Experience from JFJ: 10-25 % deviation
…

## Slide 37: Effective extraction volume correction – Formula
Application of correction:
Only on internal standard normalized data of ‘samples’ where actual filters were extracted
(i.e. not on waterblanks, QC samples like ANAS, Spiked ANAS, …)
Correction factor, >1

## Slide 38: Effective extraction volume correction – Example
Primary ion normalized
Internal standard normalized
Primary ion normalized
Internal standard normalized
…
…
Before
After

## Slide 39: Waterblank subtraction
For internal standard normalized data, for each ion subtract sample average (effective volume corrected) with it’s corresponding wb average
Primary ion normalized
Internal standard normalized
sample – wb = waterblank subtracted sample
…

## Slide 40
'Semi-Quantification’
= Scaling to ambient conditions

## Slide 41: 'Semi-Quantification’ = Scaling to ambient conditions – The concept
'Semi-Quantification’ was performed by previous workflows and partly taken over here
Goals of 'Semi-Quantification’:
Make relative ion intensities comparable between samples that were treated differently in sampling or sample preparation
  Accounted for: sampling rate and time, punch size, number of punches, extraction volume
  For JFJ samples: number of punches was different for some sample batches; rest of the parameters are consistent
Currently not implemented (used to be applied by some previous workflows):
Attempting to quantify single ion species to approximate ambient concentrations; this goes under the assumption that sensitivities of internal standard and all other ion species is comparable (which is not the case); for ambient mass concentrations, molar mass of each species needs to be known (not possible for unspecified formulas)

## Slide 42: 'Semi-Quantification’ = Scaling to ambient conditions
…
only for samples that were actually extracted